# Pre-test

## Course Title:	Plumbing / Fuel Gas (4-hour version)

Course #:

Date:			Location:

Tempered  water is defined as water having a temperature range between 85( F and _________ ?

110( F

120( F

130( F

140( F

Correct answer:  a. 110º F

True or false?  All chapters of the 2004 Florida Building Code, Plumbing contain significant changes from the 2001 Florida Building Code, Plumbing.

- true

false

Correct answer:  b. false

True or false?  Sleeving is required for installation of CPVC into concrete or similar materials.

- true

false

Correct answer:  b. false

True or false?  Freeze protection is only required where design temperature is less than 32( F.

- true

false

Correct answer:  a. true

The automatic clothes washer fixture drain shall connect to a branch drain or drainage stack a minimum of _____ inch(es) in diameter.

- 1

2

3

4

Correct answer:  c. 3

Waste outlets serving showers shall be at least _________ inch(es) in diameter.

- 1

1½

2

2½

Correct answer:  b. 1½

True or false?  All new or repaired potable water systems have to be purged of deleterious matter and disinfected prior to utilization.

- true

false

Correct answer:  b. false

True or false?  Where a trap seal is subject to loss by evaporation, a trap seal primer valve has to be installed.

- true

false

Correct answer:  a. true

True or false?  In the 2004 Florida Building Code, Residential, there is no limit on hot water distances.

- true

false

Correct answer:  a. true

True or False?  In the 2004 Florida Building Code, Residential, the developed length of the fixture drain from the trap weir to the vent fitting for self-siphoning fixtures, such as water closets, is limited.

- true

false

Correct answer:  b. false