## Slide 1
Jason Seals
Certification Manager, AAMA
Steve Orlowski:
Sr. Director of Standards and
Technical Activities, WDMA
Industry Presentation on Water Penetration Testing
Presented by AAMA & WDMA

## Slide 2
Topics of discussion
  Brief History of Water Penetration Testing Requirements
  Current Water Penetration Testing Requirements
  Impact of Water Penetration Testing on Fenestration Products

## Slide 3
Earliest records for water penetration testing…
  1955 windows tested to 15 minute exposure to 2 inches of rain per hour and a 45 mph "dynamic pressure“.
  In 1962, the minimum test pressure for water penetration testing was changed to 2.86 psf.
  Water test pressures requirements for wood windows not introduced until 1967.

## Slide 4
ASTM E331 testing method introduced in 1967
  Voluntarily Referenced in AAMA 302.6-68, AAMA 402.6-68
    HP products had WTP specified at 10% of DP (minimum of 2.86 psf)
  Voluntarily Referenced in NWMA I.S. 2-69
    WTP for following window classes and design testing
      Class A, 6.24 psf (50 mph) @ 5 gal./hr
      Class B, 2.86 psf (34 mph) @ 5 gal./hr
      Class C, 1.57 psf (25 mph) @ 5 gal./hr

## Slide 5
ASTM E547 test method introduced mid 80’s
  ANSI/AAMA 101-85
    Water test pressures were increased to 15% of the design load
    R and C tested per E547, HC tested per E331 and E547
  NWWDA I.S. 2-87
    Drops reference to E331 for WTP and references E547
    Keeps pass/fail criteria and introduces Performance Grade concepts

## Slide 6
Early 90’s Continuation of using % of design pressure for various classes
  ANSI/AAMA 101-93
    R, C, HC used WTP@ 15% of DP, tested per E547
    Introduced the AW class, used WTP @ 20% of DP per E331
  WDMA I.S. 2-93
    Established WTP @ 15% of the DP, tested per E547
  High Velocity Hurricane Zone
    TAS 202-94 WTP @ 15% of the DP for 15 minutes

## Slide 7
First edition of AAMA/WDMA 101/I.S.2-97
  Standardized both organization at 15% DP for R, LC, C, HC products, 20% for AW products
  Water applied at 5 gal/hr/ft2, equivalent to 8” of rain per hour
  Maximum WTP is now specified at 15 psf/ 2.9” HOH, 77.5 mph
  These are straight-line winds sustained over a 15-minute period normal to the fenestration- an extremely severe test

## Slide 8
  Basis for the 15% and 20% respectively…
  “The severity of this test is seen when it is realized that, according to U.S. Department of Commerce, Weather Bureau Technical Paper No. 40-1963, "Rainfall Frequency Atlas of the United States for Durations from 30 Minutes to 24 Hours and Return Periods from 1 to 100 Years", on rainfall frequency published by the National Weather Service, the greatest rainfall expected anywhere in the contiguous 48 United States for a one-hour period during a span of 50 years is less than 5 inches (125 mm) per hour.”

## Slide 9
  Current fenestration requirements strike the balance between performance, function and accessibility…
  Sliding seal products (patio doors) to maintain a reasonable threshold height to exterior landing and patio
  Window units to meet the required emergency escape/rescue opening dimensions
  Operable windows to supply natural ventilation, to meet code requirements
  Balance between a rigid weather seal and meeting operating force requirements of the code

## Slide 10
  In closing
  There are many factors that go into the design and testing of fenestration products for multiple weather conditions.
  The entire building must be evaluated as a system, not as stand alone individual components.
  The Window and Door Industry continues to support research that enhances the built environment.

## Slide 11
  Thank You
Notes: As threshold heights increase, it affects the ability of designers to meet the accessibility requirements under the ADA and A117.1.